DEPARTURE BRIEFING

1.  TOLD

Vref < Vto -- acceleration check time

50 % flap ground roll  (E)

2.  EMERGENCY PROCEDURES

Prior to refusal speed -- “reject  prop/eng/sys/load (brief description)”

- Prop - (2 of top 3, prop low oil light, directional control)

Flight idle / ESP / reverse symetricals

- anything else (no rush)

Gnd idle / reverse all 4 (if necessary) / wait ‘til safe taxi speed

After refusal speed

- Treat as an airborne emergency //// option if on long runway

- Advisory call

Prop / engine failure -- Gear , FX, Flaps

Obstacles :  gear w/i 3  //  fx w/i 6  //  3 eng climb speed to MSA

(N) keep us clear of obstacles

No obstacles :  try for 150 KTAS -- Vmca2

(E) - clear to go MECH

Engine fire / overheat -- keep it running

Anything else we’ll handle after clear from ground

Fuel dumping / bleeds  (E)

Recovery base ? (wx  bad -- IAP)

3.  SIGNALS FOR GEAR AND FLAP RETRACTION

4.  DEPARTURE

SID / RV / Clearance ALT / HDG

Nav Aids

SCNS - overview of plan

Radar Alt - (400’ or HAT)

Hazardous terrain / obstacles (N)

5.  SKE / FORMATION PROCEDURES

SKE  - (CP)

Abort Calls  -  (CP - ATC /  N - interplane)

6.  SCNS PROCEDURES

Fly in SCNS  //  Radial/ DME

7.  ADS PROCEDURES

ARRIVAL BRIEFING

VFR CHART

1.  WEATHER -- ATIS // METRO // FSS

2.  APPROACH TO BE USED

Flap setting // type landing // speeds//runway available vs. desired ldg dis.

Navaids // Obstacles // ESA//MSA?

Course

Altitudes  -- FAF / HAT/Radar Altimeter?

Descent rate

Precision : drift / gnd speed  (N)

Non-precision : 1500 fpm (CP) backup  //  Drift  (N)

Timing -- calculate and backup “hack”  (N)

Touchdown point and Landing Distance

(E) - “speed good” // “props good”

3.  BACKUP APPROACH

Vis // Loc // anything close // missed approach

4.  MISSED APPROACH

Initial hdg / alt   // (N) read the rest

(E) - call 7,8,9 or 15,16,17

 - ESP checklist				C - Configuration

Looks like another one:

 - descent/before lndg				GR DN // FLAP UP

Flap cont. CB-PULL

T - TRIM					(E) - reset CB

(E) - on final

A - AIRSPEEDS				H - Hydraulics

Normal speeds	(CP) - possible light illum.

Vmca2 / Vmca3 / Approach	Nosewheel ?

S - SIMULTANEOUS TRANS.	Brakes - Norm / emer

R - REVERSE				E - Electrics

(E) - backup	Load ?

GO AROUND

Notify				W - Weight  //  Wind

Max pwr - (E)	Dead eng up-wind

Raise dead / step on good eng

Climb profile /  flaps		(CP) - Backup A/C cont./ spd / descisions

Vmca2  to 3 eng climb		(N) - Do whatever it takes to get us on ground

Altitude